## Slide 1: CHAPTER 9
Power

## Slide 2
When something happens we say work has been done, or energy has been used.
With electricity we want to know the rate at which electrical energy is being used or consumed.
The rate at which electrical energy is being consumed is called Power (P).

## Slide 3
The unit for measuring energy is called the Joule (J) named after British scientist James Prescott Joule.
Power is how many Joules of energy are be transformed every second and we use the unit the Watt (W) after James Watt a Scottish inventor.
Ex. 60 W light bulb uses 60 J of electrical energy every second to produce 60 J of heat and light energy

## Slide 4
Another unit used to measure power is the horsepower, which is equal to the 746 W that James Watt used to help boost sales of his steam engines.

## Slide 5
We can calculate power any electrical device; however, we use voltage and current instead of energy and time. The relationship to calculate power is:
P
I V
Power
Current
Voltage

## Slide 6: Example
If a 6.0 V battery supplies a current of 2.0 A, what is the power output of the battery?
What equation are we going to use?
P=IV
P = 2.0 x 6.0
P = 12
12 what?
P = 12 W (don’t forget your units!)

## Slide 7: Practice
Do examples a-e on your own in your notes package.

## Slide 8
Many electronic devices are labeled with a power rating.
A power rating is a measurement of how much electrical energy an electrical device consumes for every second it is in use.
We can use the electrical power rating and the amount time to calculate the electrical energy a particular electrical device consumes.

## Slide 9: Formula for Power Rating
E = Pt
E = Energy transformed (J)
P = Power (W)
t = Time (seconds)

## Slide 10: Converting Time
Before we move on – How do you get time into seconds?
Ex. 7 min
How many seconds are in 7 min?

## Slide 11: Example
E = Pt
How much electrical energy does a 1200 W hair dryer if it is used for 5.0 min consume?
Remember time has to be in seconds!
5 min x
E =
(1200)
(300)
E = 360 000
J

## Slide 12: Practice
Do examples a-c on your own in your notes package

## Slide 13
Since the energy consumed by most electrical devices is often quite large a special unit is used called the kilowatt-hour (kWh).
There are 1000 W in a kW and 3600 seconds (s) in an hour (h). The power companies charge users a fee for every kilowatt-hour a customer uses.
kWh = (total hours x W)
        1000

## Slide 14: x
To calculate the cost of energy used we use the following formula:

## Slide 15: Practice
Try examples a-e in your notes package